## Slide 1
Millimeter-Wave Near-Field
SAR Imaging
Muhammet Emin Yanik and Murat Torlak
Department of Electrical & Computer Engineering
The University of Texas at Dallas
(muhammet.yanik@utdallas.edu)
3D MIMO-SAR Imaging
3D Simulation Toolset

## Slide 2
3-D SAR Simulation GUI
STL object to SAR simulation tool
Import STL object to MATLAB

## Slide 3
3-D SAR Simulation GUI
STL object to SAR simulation tool
Convert to point cloud
Get voxel data

## Slide 4
3-D SAR Simulation GUI
STL object to SAR simulation tool
Downsample
Define Range of Interest (crop z-axis)
Reduce number of voxels

## Slide 5
3D MIMO-SAR Simulations
Array configuration: IWR1443-Boost, 2Tx, 4Rx
77 GHz 5000 ksps
70.295 MHz/µs 4.66 µs
N 256 samples B 3.585 GHz
400 mm
Volume rendering
MIP
MIP (Jet)

## Slide 6
Effect of Bandwidth
Same SAR parameters, larger bandwidth:
77 GHz 2000 ksps
150 MHz/µs 0 µs
N 256 samples B 19.125 GHz
Point cloud
3-D Volume Image
x-z slice
y-z view
MIP

## Slide 7
Effect of Bandwidth
Same SAR parameters, same target, lower bandwidth:
77 GHz 2000 ksps
150 MHz/µs 0 µs
N 128 samples B 9.523 GHz
3-D Volume Image
MIP
y-z view